|  | SCS Static Control Systems Electronic and Automation |
| --- | --- |

UFS 15-22-40-110

BRAKING UNIT

CONTENTS

0. WORK SAFETY	3

0.1 EMC Requirements	4

1. WORKING DESCRIPTION	5

1.1 Alarm leds	6

1.2 Switching ON and OFF	6

2. MODEL AND DIMENSIONS	7

2.1 Outline dimensions	7

2.2 Wiring terminals	7

2.3 Installation	8

3. CONNECTIONS	9

3.1  Connections  UFSxx/UFSxxJ	9

4.  FEATURES AND PERFORMANCES	10

4.1 General Technical Features	10

4.2 Features of UFSxx version	10

4.3 Dissipated power by UFSxx versions	10

4.4 Exclusion of the thermal relay and continual service working	11

5. STANDARD APPLICATION TABLE	12

5.1 Standard braking resistances	12

6. BOARD THERMAL DIMENSIONING	13

7.  VARIANTS AND CONFIGURATIONS	14

7.1 Technical features of the UFSxxJ version	14

7.2   Max. dissipated power – UFSxxJ version	14

7.3   Standard applicative table for   UFSxxJ	14

7.4  Starndard brake resistors for	15

7.5 Configuration of the UF braking voltage by means of the DIP-SW	15

8. CONNECTION of many BRAKING UNITS ON AN INVERTER	16

# 0. WORK SAFETY

STATEMENT

This braking unit was designed, based on the EEC directives applicable to it, that is to say:

•	Low voltage directive No.  73/23 - 93/68

•	Machine directive 89/392 - 91/368 - 93/44

This is a complex component aimed at being integrated into the equipment by skilled staff only. This equipment can be used in industrial areas only.

It must be connected to the relevant inverter. It can cause troubles to radio-frequencies.

This equipment must be used, installed and managed by skilled and qualified staff, familiar with its application and working. The usage will be compliant with provisions stated in:

- PRODUCT STANDARDS (if set)

- BASIC CEI EN 60204-1 STANDARD

- RUNNING LAWS

- THIS MANUAL

To the safety purpose, some basic provisions should be recalled:

- ALWAYS FORESEE A SECTIONING MEAN FROM THE POWER SUPPLY NETWORK

- PROVIDE ELECTRIC AND NON-ELECTRIC GUARDS TO PREVENT DAMAGES TO PEOPLE AND GOODS IN CASE OF EQUIPMENT FAILURE.

SCS rejects any responsibilities for direct and indirect damages linked to the unproper usage of this option.

DANGER: ELECTRICAL SHOCKS

NOTE: The contents of this manual when printing it, is to be considered as correct.

However the manufacturer is entitled to change its contents without any notice.

## 0.1 EMC Requirements

Even if SCS considers this product as a complex component this braking unit was designed to match requirements as per provisions in CEI EN 50081-2 standard (Emission) and CEI EN 50082-2 standard (Immunity). It was tested in an independent laboratory and trials gave a positive outcome. Consequently, the CE mark on the product serial number label is valid both for the CE LVD 73/23 93/68 directive (low voltage, safety) and for the EEC EMC 89/336 directive (electromagnetic compatibility).

This equipment is an outside option for inverter and works in a strict coordination with its related inverter from which it receives control and power supply.

Since there is no direct connection with the power supply network, this equipment contribution to EMC emissions is negligible since these latter are fully absorbed by the inverter power supply filter (refer to the inverter user’s guide).

Mount the braking unit close to its relevant inverter, minding to create with this a mutual low impedance and high frequency earthing (ex. the surface of the mounting plate). The connection to the braking resistor must be as short as possible and will be performed using a braided or shielded cable. Braking resistor will have a metal screen or will be armoured in order to filter emissions. To have further execution detail, please apply to our guide NT247A.

The end verification in the conformity of emission and immunity EMC standard for the specific product and/or to the full installation applicable to it, are under the manufacturer’s and/or the end installer’s province.

# 1. WORKING DESCRIPTION

The UFS braking units ... are conceived to be joined with the Mitsubishi inverter, FREQROL  MELTRAC series. However, they can be used with inverters or converters equipped with BUS-DC.

These packages aim at dissipating, through a control chopper, the energy coming from the load  (kinetic energy during the braking phase). Normally, this energy produces a rise of the inverter Bus DC and this value cannot exceed a given limit. The instantaneous power that can be absorbed is sent to a group of power resistors. Every group is self-supplied by the inverter Bus DC.

The UFS braking units  are equipped with circuit for synchronization (through the two-wire cable connection) for the Master/Slave connection of more parallel units. By means of this circuit it is possible to increase  the total brake power, connecting more units – also of different  sizes -  to the same BUS-DC, provided that each unit is connected to the resistor group that  is specific for that UFS size.

In order to protect the external braking resistors,on the UFS standard unit a suitable electro-mechanical thermal relay is mounted with insulated auxiliary contacts which are available to operate the alarm sequences.

For the brake unit protection, on the heat sink a bimetal thermostat is mounted and internally connected, whose intervention causes the temporary deactivation of the unit.

The braking power is to be dimensioned in function of the actual braking cycle, considering pauses. The braking power is given by:

Power ‘P’ in watt, speed ‘W’ in rad/sec, time ‘t’ in sec., moment of inertia ‘J’ in Kg*m2  to the motor axis.

Obviously, the stated power is to be reduced by the power necessary for the working. This latter contributes to brake the load. In its turn, the motor thermally absorbs 10% approx. of the nominal power, due to its inside leaks. Considering pauses, the mean power will become:

Used resistors must be able to dissipate at least the continual service power. The power values shown on the table provide for a quite hard engagement (braking for 15 seconds approx. and 150 seconds pause). These can be reduced provided that the application requires it. In this event, the thermal relay is to be delayed in function of the maximum power that every resistor can dissipate.

## 1.1 Alarm leds

The green ‘ON’ led states that the braking unit is supplied by the DC source. Usually, it is lighted.

The red ‘BR’ led lights on when the unit transfers energy coming on the load on resistors. Usually it is switched off, but it blinks when the unit is working.

## 1.2 Switching ON and OFF

The unit is equipped with a circuit which directly takes the power supply from the BUS-DC to which it is connected (P and N terminal boards). In order to avoid spurious switching ON of the braking circuit, the inside enabling is delayed by 300mS versus the voltage arrival of the BUS-DC voltage to the nominal value.

This delay is not working in case of very short power failures (400mS).

# 2. MODEL AND DIMENSIONS

## 2.1 Outline dimensions

#### UFS15 / 15J / 22 / 22J / 40 / 40J

| Variable dimensions according to size | Weight |
| --- | --- |
| Model | Quote |  |
|  | W | L1 | H |  |
| UFS15,22,40 UFS15J,22J,40J | 100 | / | 175 | 2.5 Kg |
| UFS110 | 107 | 270 | 195 | 3.9 Kg |

## 2.2 Wiring terminals

- UFS15,UFS22,UFS40,UFS15J,UFS22J,UFS40J

Outside terminal 2,5 sq.mm.

3	= thermal relay common

- = NA inside  thermal relay contact

- = NC inside thermal relay contact

Outside terminal 6 sq.mm.

P/P1 	= Positive terminal of Bus-DC

N	= Negative terminal of Bus-DC

F	= Braking resistors terminal

G/Y	= yellow/green terminal for power earth

Inside terminals can be reached by removing the product transparent cover

M1 terminal on the printed circuit board

M1-1	= Connection inside thermostat

M1-2	= Connection inside thermostat

M4 terminal on the printed circuit board – synchronism command input

M4-1	= INA

M4-2	= INB

M5 terminal on the printed circuit board – synchronism command output

M5-1	= OUTA

M5-2	= OUTB

- UFS110

Outside terminal 16 sq.mm.

P/P1 	= Positive terminal of Bus-DC

N	= Negative terminal of Bus-DC

F	= Braking resistors terminal

G/Y	= yellow/green terminal for power earth

Inside terminals can be reached by removing the product transparent cover

M1 terminal on the printed circuit board

M1-1	= Connection inside thermostat

M1-2	= Connection inside thermostat

M4 terminal on the printed circuit board – synchronism command input

M4-1	= INA

M4-2	= INB

M5 terminal on the printed circuit board – synchronism command output

M5-1	= OUTA

M5-2	= OUTB

The contacts of the inside thermic can be reached by removing the product transparent cover

97-98 =  NO contact of inside thermic

95-96 =  NC contact of inside thermic

## 2.3 Installation

- The units are designed to work under natural ventilation. When installing the unit, please provide for a sufficient area to make the air circulate. Then match with an assembling pitch by 150 mm. (horizontal) and 400 mm. (vertical).

If the units are installed next to other heat generating units, verify that the air temperature does not exceed the maximum working temperature stated at the paragraph on technical features.

- In case they are installed near other apparatuses which emanate heat, please ensure that the

ar temperature does not exceed the max. operating temperature, which is indicated in the technical features paragraph.

# 3. CONNECTIONS

## 3.1  Connections  UFSxx/UFSxxJ

Figure 4.1 UFS standard connection

P.S: The connections between + (P), - (N) of the inverter and P, N of the brake unit and between P, F and the RF resistors must be done using braided cables not longer than  5 meters.

# 4.  FEATURES AND PERFORMANCES

## 4.1 General Technical Features

- Tolerance on the intervention voltage: 0.8%

- Hysteresis : 15V

- Ambient temperature 0°C ( 40°C

- maximum braking time = 10s

- Protection degree IP20

- Thermal guard  with manual / automatic reset

## 4.2 Features of UFSxx version

- Power supply voltage 450Vdc-650Vdc

- Maximum voltage 800Vdc

| Unit | Braking voltage | Maximum peak current IP (A) | Maximum instantaneous power Pmax (KW) | Standard Ith (A) | %ED Max | RF(() min. |
| --- | --- | --- | --- | --- | --- | --- |
| UFS15 | 745 | 18 | 14 | 4(6 | 10% | >40 |
| UFS22 | 745 | 34 | 25 | 7(11 | 10% | >24 |
| UFS40 | 745 | 55 | 41 | 12(18 | 10% | >13,5 |
| UFS110 | 745 | 140 | 105 | 23(32 | 10% | >5,5 |

Used resistor models must allow a very-high over-chargeability (20/1). Cement-made corrugated belt models are the best.

## N.B. The resistors values indicated, are referred to the units setted on the standard threshold voltage (745V)

## 4.3 Dissipated power by UFSxx versions

- Power dissipated with the unit in stand-by mode @650Vdc: 25W

- Power dissipated when braking; with thermal current = standard Ith

| UFS15 | UFS22 | UFS40 | UFS110 |
| --- | --- | --- | --- |
| 52W | 64W | 79W | 85W |

P.S.:The stated dissipated powers do not include the power dissipated by external braking resistors.

## 4.4 Exclusion of the thermal relay and continual service working

If the thermal relay (external or internal) is unconnected, the braking package can work in continual service at the lc. current. In this event, the outside resistors will be value modified in order that they cannot exceed the Ic. Their minimum values will be those shown on the following table:

| Unit | Resistor for continual service | IC (A) |
| --- | --- | --- |
| UFS15 | 50( - 14KW in die cast or tungsten | 15 |
| UFS22 | 33( - 20KW in die cast or tungsten | 22 |
| UFS40 | 25( - 33KW in die cast or tungsten | 30 |
| UFS110 | 17( -42KW in die cast or tungsten | 44 |
| UFS15J | 25( - 7KW in die cast or tungsten | 15 |
| UFS22J | 17( - 10 KW in die cast or tungsten | 22 |
| UFS40J | 13( - 15 KW in die cast or tungsten | 30 |

Note: Value of resistors in the table, are vaild only for the units setted at the standard braking threshold (SW4 = ON , 745V).

The exclusion of the inside thermal relay in the UFS unit includes the changing in the wiring of such relay. The elements of the thermal relay are to be short-circuited using cables of the same section than those present in the unit. The outside resistors are to be guarded with fuses or automatic magneto-thermal switches fit to mounted resistors, and at least with the same IC current, if they are used under this condition.

# 5. STANDARD APPLICATION TABLE

In the below table is reported an indicative pairing, obtained from the motor power and from the braking torque percentage in comparison with the rated torque.  The pairing is only indicative and, to be sure that  the braking units application will not cause problems, it is necessary to check the machine while operating or to calculate exactly the regenerative energy during the braking phase.

| Braking torque | Motor power (kW) |
| --- | --- |
|  | 5,5 | 7,5 | 11 | 15 | 18,5 | 22 | 30 | 37 | 45 | 55 | 75 | 90 | 110 | 132 | 160 | 220 | 280 |
| 150 % - 5 sec. | UFS 15 | UFS 22 | UFS40 | UFS110 | 2 x UFS110 | 3 x UFS110 |
| 100% - 15 sec. | UFS15/UFS22 | UFS22 | UFS40 | UFS110 | 2 x UFS110 |
| 50% - 15 sec. | UFS15 | UFS22 | UFS40 | UFS110 | 2 x UFS110 |

## 5.1 Standard braking resistances

Since many aplications require a working cycle with a braking time shorter than 2s and a pause time at least of 40s (E.D. =5%), braking units UFSxx are provided with standard resistors that, if used according to the following directions, allow to dissipate the energy coming from the motor.

| Unit | SCS kit | Connection | Overall Resistance | Overall power continuous duty S1 | Overall power intermittent duty S3 %ED 5% (Max 2” cont.)* | Dimensions 1 pc L/W/H. |
| --- | --- | --- | --- | --- | --- | --- |
| UFS15 | RUFC15 | 1 pz. x 40( 1200W |  | 40( -0%+10% | 1,2 kW | 14kW | 310/100/75 |
| UFS22 | RUFC22 | 1 pz x 24( 2000W |  | 24( -0%+10% | 2 kW | 25kW | 365/100/75 |
| UFS40 | RUFC40 | 2 pz. x 6,8( 2000W |  | 13,6( -0%+10% | 4 kW | 41kW | 365/100/75 |
| UFS110 | RUFC110 | 4 pz. x 6,8( 2000W |  | 6,8( -0%+10% | 8 kW | 82kW | 365/100/75 |

*Attention! The UFSxx units can tolerate working cycles harder the the one described for the SCS kit. Thus, If necessary, one can use the braking units with resistors different from those given in the SCS kit. When using other resistor values, NEVER mount ohm values lower than those stated at the paragraph 4.2 , since this can damage the unit.

# 6. BOARD THERMAL DIMENSIONING

At the end of the braking stage, the RF resistor can reach even very high surface temperatures (max. 450°C). Place them in danger-free areas and far from products which could be interested in the heat flow. The energy absorbed by the resistor is the following one:

E = in Joule	Pmax = in watt	t=in seconds

Remember that 1K calory is equal to 4187 Joules, or 1,16*10E-3KW/h  (1KW = 860Kcal), and these latter are to be considered for the heat disposal and the dimensioning of the ventilation in the electrical board. One can consider a mean power in function  of the processing cycle that, in the worst case, is equal to the maximum P power of the resistor stated in the table, for the RF standard version.

The necessary ventilation, considered in the board thermal exchange, is given by:

Q = cubic meters/hour	 P  = power in KW   (T° = environment/board thermal drop (generally 3(5°C).

# 7.  VARIANTS AND CONFIGURATIONS

## 7.1 Technical features of the UFSxxJ version

The “J” version is identical to the previous one but the rated level threshold is  375V and is suitable for mains voltages  210(230V (10%.

- Power suopply voltage 234Vdc(357Vdc

- Max. voltage 400Vdc

| Unit | Braking voltage | Max, peak current IP (A) | Max. istantaneous power Pmax (KW) | Ith (A) standard | %ED | RF(() min. |
| --- | --- | --- | --- | --- | --- | --- |
| UFS15J | 375 | 18 | 6,7 | 4(6 | 10% | >21 |
| UFS22J | 375 | 34 | 12.7 | 7(11 | 10% | >11 |
| UFS40J | 375 | 55 | 20 | 12(18 | 10% | >6.8 |

## N.B. The resistors values indicated, are referred to the units setted on the standard threshold voltage (374V)

## 7.2   Max. dissipated power – UFSxxJ version

- Dissipated power (unit in  stand-by mode) @ 375Vdc: 14W

- Dissipated power during braking; with thermic current = Ith standard

| UFS15J | UFS22J | UFS40J |
| --- | --- | --- |
| 32W | 44W | 59W |

## 7.3   Standard applicative table for   UFSxxJ

In the below reported table an indicative coupling is shown, obtained from the motor powers and from the braking torque percentage in comparison to the rated torque. Such a coupling is only indicative, and to be sure that the application of the brake units will not cause problems, it’s necessary to carry out a check on the machine operation, or a precise calculation of the energy which is regenerated during the braking phase.

| Brake torque | Motor power |
| --- | --- |
|  | 5,5 | 7,5 | 11 | 15 | 18,5 | 22 | 30 | 37 | 45 | 55 |
| 150% - 5 sec | UFS15J | UFS22J | UFS40J | 2xUFS40J |
| 100% - 15 sec. | UFS15J / UFS22J | UFS22J | UFS40J | 2xUFS40J |
| 50% - 15 sec. | UFS15J | UFS22J | UFS40J | 1UFS40J+ 1UFS15J |

## 7.4  Starndard brake resistors for UFS xx J

| Unit | SCS Kit | Connection | Total resistance | Total power S1 continuous service | Total power S3 cyclic service %ED 5% (Max 2” continuous)* | Dimensions 1 piece L/W/H. |
| --- | --- | --- | --- | --- | --- | --- |
| UFS15J | RUFC15J | 1 pz. x 24( 800W |  | 24( (5% | 0.8kW | 6kW | 240x100x75 |
| UFS22J | RUFC22J | 1 pz x 12( 1200W |  | 12( (5% | 1.2 kW | 12kW | 310x100x75 |
| UFS40J | RUFC40J | 1 pz. X7.5( 2000W |  | 7.5( (5% | 2kW | 19kW | 365x100x75 |

Attention!

P.S.: When using other values for resistance, NEVER mount ohm values lower than those shown at the paragraph of the technical features, because this can damage the unit.

## 7.5 Configuration of the UF braking voltage by means of the DIP-SW

The unit is equipped with  8 microswitches, by which it is possible to set a braking value different from the standard one, as indicated in the following table. In the table, to clarify as much as possible, the voltage values for the activationa and deactivation (SLAVE) of the unit are reported.

| SW1 | UFSxx | UFSxxJ |
| --- | --- | --- |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | Braking on | Braking off | Braking on | Braking off |
| on | off | off | off | off | off | off | off | 778 | 764 | 390 | 384 |
| off | on | off | off | off | off | off | off | 770 | 757 | 386 | 380 |
| off | off | on | off | off | off | off | off | 754 | 740 | 379 | 371 |
| off | off | off | on | off | off | off | off | 745 | 730 | 374 | 367 |
| off | off | off | off | on | off | off | off | 726 | 710 | 364 | 357 |
| off | off | off | off | off | on | off | off | 703 | 690 | 353 | 346 |
| off | off | off | off | off | off | on | off | 690 | 677 | 347 | 340 |
| off | off | off | off | off | off | off | on | slave | slave | slave | slave |

SW1 – 4 (S1) = ON standard position.

# 8. CONNECTION TO MORE BRAKING UNITS ON AN INVERTER

In case the power of a single braking unit should not be sufficient any longer for the foreseen application, it is possible to connect more braking units to the same BUS-DC.

To do this it’s necessary to use one standard UFS, which operates as MASTER unit, and other UFS units, configured as SLAVE units.

The only operation that is necessary to carry out on the standard UFS units, in order to configure

Them in the SLAVE mode, is that of deactivate the autonomous braking (turn the switch N°8 of the Dip-Switch SW1 to the “On” position).

The UFS units are provided with two output terminals, to propagate the brake command  to other UFS units, and with two input terminals which accept the current command coming from the MASTER unit or from a SLAVE unit preceding it. Please see the connection diagram hereafter reported. The brake command is delayed for about 0,1 mS. This allows to attenuate the switching disturb which would occur when switching contemporarily all the UFS units connected to the same BUS-DC, and it’s  a negligible time lag considering the normal operating cycle of the drive.

In case that five UFS units are used, the last UFS will start operating after 0,4 mS.

The max. number of UFS that can be connected in this way is 5 (1 MASTER and 4 Slave).

It’s possible also to connect different UFS sizes  (i.e.: 1 UFS110 and 1 UFS40), provided that each unit is connected to the brake resistor which is suitable for that size, using for example the kit supplied by SCS. The UFS units are not protected against short-circuits and therefore if a resistor is not properly connected, this can  seriously damage the unit.

Fig. 8.1 UFS connections under MASTER/SLAVE configuration